## Slide 1
Chapter 1
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Background
The Game Plan
The Art of Managing Complexity
The Digital Abstraction
Number Systems
Logic Gates
Logic Levels
CMOS Transistors
Power Consumption
Chapter 1 :: Topics

## Slide 3
Microprocessors have revolutionized our world
  Cell phones, Internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billion in 1985 to $306 billion in 2013
Background

## Slide 4
Purpose of course:
Understand what’s under the hood of a computer
Learn the principles of digital design
Learn to systematically debug increasingly complex designs
Design and build a microprocessor
The Game Plan

## Slide 5
Abstraction
Discipline
The Three –y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 6
Hiding details when they aren’t important
Abstraction

## Slide 7
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors: i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 8
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -y’s

## Slide 9
Hierarchy
  Three main modules: lock, stock, and barrel
  Submodules of lock: hammer, flint, frizzen, etc.
Example: The Flintlock Rifle

## Slide 10
Modularity
  Function of stock: mount barrel and lock
  Interface of stock: length and location of mounting pins
Regularity
  Interchangeable parts
Example: The Flintlock Rifle

## Slide 11
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 12
Designed by Charles Babbage from 1834 – 1871
Considered to be the first digital computer
Built from mechanical gears, where each gear represented a discrete value (0-9)
Babbage died before it was finished
The Analytical Engine

## Slide 13
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 14
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT
George Boole, 1815-1864

## Slide 15
Decimal numbers
Binary numbers
Number Systems

## Slide 16
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two
Handy to memorize

## Slide 17
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 18
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
Decimal to Binary Conversion

## Slide 19
  5310
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012
Decimal to Binary Conversion

## Slide 20
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
or
75/2 = 37 R1
37/2 = 18 R1
18/2 = 9 R0
9/2 = 4 R1
4/2 = 2 R0
2/2 = 1 R0
1/2 = 0 R1
Decimal to Binary Conversion

## Slide 21
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 22
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 23
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 24
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 25
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 26
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 27
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 28
Decimal
Binary
Addition

## Slide 29
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 30
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 31
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 32
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 33
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 34
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 35
msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers
+

## Slide 36
“Taking the Two’s complement” flips the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 37
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 38
Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 39
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 40
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 41
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 42
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 43
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 44
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 45
Single-Input Logic Gates

## Slide 46
Two-Input Logic Gates

## Slide 47
More Two-Input Logic Gates

## Slide 48
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 49
Multi-input XOR: Odd parity
SystemVerilog Description
module gates(input logic a, b, c,
output logic y1, y2, y3, y4, y5);
not g1(y1, a);
and g2(y2, a, b);
or g3(y3, a, b, c);
nand g4(y4, b, c);
xor g5(y5, a, c);
endmodule

## Slide 50
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 51
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 52
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 53
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 54
Noise Margins

## Slide 55
High Noise Margin: NMH = VOH – VIH
Low Noise Margin: NML = VIL – VOL
Noise Margins

## Slide 56
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
DC Transfer Characteristics
NMH, NML < VDD/2

## Slide 57
DC Transfer Characteristics

## Slide 58
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
VDD Scaling

## Slide 59
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof: if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 60
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 61
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 62
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 63
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 64
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 65
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 66
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 67
Transistor Function

## Slide 68
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 69
CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0

## Slide 70
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 71
CMOS Gate Structure

## Slide 72
NOR3 Gate
How do you build a three-input NOR gate?

## Slide 73
AND2 Gate
How do you build a two-input AND gate?

## Slide 74
nMOS pass 1’s poorly
pMOS pass 0’s poorly
Transmission gate is a better switch
  passes both 0 and 1 well
When EN = 1, the switch is ON:
  EN = 0 and A is connected to B
When EN = 0, the switch is OFF:
  A is not connected to B
Transmission Gates

## Slide 75
Replace pull-up network with weak pMOS transistor that is always on
pMOS transistor: pulls output HIGH only when nMOS network not pulling it LOW
Pseudo-nMOS Gates

## Slide 76
Pseudo-nMOS NOR4
Pseudo-nMOS Example

## Slide 77
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Gordon Moore, 1929-

## Slide 78
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .” (Robert Cringely, Infoworld)
– Robert Cringley
Moore’s Law

## Slide 79
Power = Energy consumed per unit time
Dynamic power consumption
Static power consumption
Power Consumption

## Slide 80
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f: transistors switch (from 1 to 0 or vice versa) at that frequency
  Capacitor is charged f/2 times per second (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = ½CVDD2f
Dynamic Power Consumption

## Slide 81
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 82
Estimate the power consumption of a mobile phone running Angry Birds
  VDD = 0.8 V
  C = 5 nF
  f = 2 GHz
  IDD = 10 mA
P = ½CVDD2f + IDDVDD
= ½(5 nF)(0.8 V)2(2 GHz) + (10 mA)(0.8 V)
= (3.2 + 0.008) W ≈ 3.2 W
Power Consumption Example