## Slide 1
Chapter 3
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 3 :: Topics
Introduction
Latches and Flip-Flops
Synchronous Logic Design
Finite State Machines
Timing of Sequential Logic
Parallelism

## Slide 3
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about past inputs necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops
Introduction

## Slide 4
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 5
The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 6
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit

## Slide 7
Consider the two possible cases:
  Q = 0:
  then Q = 0, Q = 1 (consistent)
  Q = 1:
  then Q = 1, Q = 0 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis

## Slide 8
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch

## Slide 9
  S = 1, R = 0:
  then Q = 1 and Q = 0
  Set the output
  S = 0, R = 1:
  then Q = 0 and Q = 1
  Reset the output
SR Latch Analysis
1
1

## Slide 10
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis
1

## Slide 11
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  (S = 1, R = 0, Q = 1)
  Reset: Make the output 0
  (S = 0, R = 1, Q = 0)
Avoid invalid state
(when S = R = 1)
SR Latch Symbol

## Slide 12
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch

## Slide 13
D Latch Internal Circuit

## Slide 14
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
Activated on the clock edge
D Flip-Flop

## Slide 15
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit

## Slide 16
D Latch vs. D Flip-Flop

## Slide 17
Registers: Multi-bit Flip-Flop

## Slide 18
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops

## Slide 19
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops

## Slide 20
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 21
Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop

## Slide 22
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops

## Slide 23
Sequential circuits: all circuits that aren’t combinational
A problematic circuit:
No inputs and 1-3 outputs
Astable circuit, oscillates
Period depends on inverter delay
It has a cyclic path: output fed back to input
Sequential Logic

## Slide 24
Multi-input XOR: Odd parity
SystemVerilog Description
module flop(input logic clk, d,
output logic q);
always_ff @(posedge clk)
q <= d;
endmodule

## Slide 25
Multi-input XOR: Odd parity
SystemVerilog Description
module flopenr(input logic clk, en, reset, d,
output logic q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (en) q <= d;
endmodule

## Slide 26
Multi-input XOR: Odd parity
SystemVerilog Description
module flopenr #(parameter WIDTH = 4)
(input logic clk, reset, en,
input logic [WIDTH-1:0] d,
output logic [WIDTH-1:0] q);
always_ff @(posedge clk, posedge reset)
if (reset) q <= 0;
else if (en) q <= d;
endmodule

## Slide 27
Breaks cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge: system synchronized to the clock
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit
  At least one circuit element is a register
  All registers receive the same clock signal
  Every cyclic path contains at least one register
Two common synchronous sequential circuits
  Finite State Machines (FSMs)
  Pipelines
Synchronous Sequential Logic Design

## Slide 28
Consists of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
    Computes the outputs
Finite State Machine (FSM)

## Slide 29
Next state determined by current state and inputs
Two types of finite state machines differ in output logic:
  Moore FSM: outputs depend only on current state
  Mealy FSM: outputs depend on current state and inputs
Finite State Machines (FSMs)

## Slide 30
Traffic light controller
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
FSM Example

## Slide 31
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB
FSM Black Box

## Slide 32
FSM State Transition Diagram
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs

## Slide 33
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 34
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
FSM State Transition Table

## Slide 35
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table
S'1 = S1 xor S0
S'0 = S1S0TA + S1S0TB

## Slide 36
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0

## Slide 37
FSM Schematic: State Register

## Slide 38
FSM Schematic: Next State Logic

## Slide 39
FSM Schematic: Output Logic

## Slide 40
Multi-input XOR: Odd parity
SystemVerilog Description
module trafficFSM(input logic clk, reset,
input logic ta, tb,
output logic [1:0] la, lb);
logic [1:0] state, nextstate, sb;
logic tab, tbb, p1, p2;
// state register
flopr #(2) statereg(clk, reset, nextstate, state);
// next state logic
not n0(sb[0], s[0]);
not n1(sb[1], s[1]);
not n2(tab, ta);
not n3(tbb, tb);
xor x1(nextstate[1], state[0], state[1]);
and a1(p1, sb[0], sb[1], tab);
and a2(p2, sb[0], s[1], tbb);
or o1(nextstate[0], p1, p2);
// output logic
buf b1(la[1], s[1]);
and a3(la[0], s[0], sb[1]);
inv n4(lb[1], s[1]);
and a4(lb[0], s[0], s[1]);
endmodule

## Slide 41
FSM Timing Diagram

## Slide 42
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler
FSM State Encoding

## Slide 43
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01. Design Moore and Mealy FSMs of the snail’s brain.
Moore vs. Mealy FSM

## Slide 44
Mealy FSM: arcs indicate input/output
State Transition Diagrams

## Slide 45
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table
S1’ = S0A
S0’ = A

## Slide 46
Moore FSM Output Table
Y = S1
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1

## Slide 47
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
State | Encoding
S0 | 0
S1 | 1
Mealy FSM State Transition & Output Table
S0’ = A
Y = S0 A

## Slide 48
Moore Mealy

## Slide 49
Moore & Mealy Timing Diagram

## Slide 50
Break complex FSMs into smaller interacting FSMs
Example: Modify traffic light controller to have Parade Mode.
  Two more inputs: P, R
  When P = 1, enter Parade Mode & Bravado Blvd light stays green
  When R = 1, leave Parade Mode
Factoring State Machines

## Slide 51
Unfactored FSM
Factored FSM
Parade FSM

## Slide 52
Unfactored FSM

## Slide 53
Factored FSM

## Slide 54
Identify inputs and outputs
Sketch state transition diagram
Write state transition table
Select state encodings
For Moore machine:
  Rewrite state transition table with state encodings
  Write output table
5. For a Mealy machine:
  Rewrite combined state transition and output table with state encodings
6. Write Boolean equations for next state and output logic
7. Sketch the circuit schematic
FSM Design Procedure

## Slide 55
Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge
If not, metastability can occur
Timing

## Slide 56
Setup time: tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time: thold = time after clock edge data must be stable
Aperture time: ta = time around clock edge data must be stable (ta = tsetup + thold)
Input Timing Constraints

## Slide 57
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
Output Timing Parameters

## Slide 58
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge
Specifically, inputs must be stable
  at least tsetup before the clock edge
  at least until thold after the clock edge
Dynamic Discipline

## Slide 59
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements
Dynamic Discipline

## Slide 60
Depends on the maximum delay from register R1 through combinational logic to R2
The input to register R2 must be stable at least tsetup before clock edge
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
Setup Time Constraint
(tpcq + tsetup): sequencing overhead

## Slide 61
Depends on the minimum delay from register R1 through the combinational logic to R2
The input to register R2 must be stable for at least thold after the clock edge
thold < tccq + tcd
tcd > thold - tccq
Hold Time Constraint

## Slide 62
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!
Timing Analysis

## Slide 63
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Timing Analysis
Add buffers to the short paths:

## Slide 64
The clock doesn’t arrive at all registers at same time
Skew: difference between two clock edges
Perform worst case analysis to guarantee dynamic discipline is not violated for any register – many registers in a system!
Clock Skew

## Slide 65
In the worst case, CLK2 is earlier than CLK1
Tc ≥ tpcq + tpd + tsetup + tskew
tpd ≤ Tc – (tpcq + tsetup + tskew)
Setup Time Constraint with Skew

## Slide 66
In the worst case, CLK2 is later than CLK1
tccq + tcd > thold + tskew
tcd > thold + tskew – tccq
Hold Time Constraint with Skew

## Slide 67
Asynchronous (for example, user) inputs might violate the dynamic discipline
Violating the Dynamic Discipline

## Slide 68
Bistable devices: two stable states, and a metastable state between them
Flip-flop: two stable states (1 and 0) and one metastable state
If flip-flop lands in metastable state, could stay there for an undetermined amount of time
Metastability

## Slide 69
Flip-flop has feedback: if Q is somewhere between 1 and 0, cross-coupled gates drive output to either rail (1 or 0)
Metastable signal: if it hasn’t resolved to 1 or 0
If flip-flop input changes at random time, probability that output Q is metastable after waiting some time, t:
P(tres > t) = (T0/Tc ) e-t/τ
tres : time to resolve to 1 or 0
T0, τ : properties of the circuit
Flip-Flop Internals

## Slide 70
Intuitively:
  T0/Tc: probability input changes at a bad time (during aperture)
P(tres > t) = (T0/Tc ) e-t/τ
  τ: time constant for how fast flip-flop moves away from metastability
P(tres > t) = (T0/Tc ) e-t/τ
If flip-flop samples metastable input, if you wait long enough (t), the output will have resolved to 1 or 0 with high probability.
Metastability

## Slide 71
Asynchronous inputs are inevitable (user interfaces, systems with different clocks interacting, etc.)
Synchronizer goal: make the probability of failure (the output Q still being metastable) low
Synchronizer cannot make the probability of failure 0
Synchronizers

## Slide 72
Synchronizer: built with two back-to-back flip-flops
Suppose D is transitioning when sampled by F1
Internal signal D2 has (Tc - tsetup) time to resolve to 1 or 0
Synchronizer Internals

## Slide 73
For each sample, probability of failure is:
P(failure) = (T0/Tc ) e-(Tc - tsetup)/τ
Synchronizer Probability of Failure

## Slide 74
If asynchronous input changes once per second, probability of failure per second is P(failure).
If input changes N times per second, probability of failure per second is:
P(failure)/second = (NT0/Tc) e-(Tc - tsetup)/τ
Synchronizer fails, on average, 1/[P(failure)/second]
Called mean time between failures, MTBF:
MTBF = 1/[P(failure)/second] = (Tc/NT0) e(Tc - tsetup)/τ
Synchronizer Mean Time Between Failures

## Slide 75
Suppose: Tc = 1/500 MHz = 2 ns τ = 200 ps
T0 = 150 ps tsetup = 100 ps
N = 10 events per second
What is the probability of failure? MTBF?
P(failure) = (150 ps/2 ns) e-(1.9 ns)/200 ps
= 5.6 × 10-6
P(failure)/second = 10 × (5.6 × 10-6 )
= 5.6 × 10-5 / second
MTBF = 1/[P(failure)/second] ≈ 5 hours
Example Synchronizer

## Slide 76
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line
Parallelism

## Slide 77
Token: Group of inputs processed to produce group of outputs
Latency: Time for one token to pass from start to end
Throughput: Number of tokens produced per unit time
Parallelism increases throughput
Parallelism Definitions

## Slide 78
Ben Bitdiddle bakes cookies to celebrate traffic light controller installation
5 minutes to roll cookies
15 minutes to bake
What is the latency and throughput without parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour
Parallelism Example

## Slide 79
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa P. Hacker to help, using her own oven
  Temporal parallelism:
    two stages: rolling and baking
    He uses two trays
    While first batch is baking, he rolls the second batch, etc.
Parallelism Example

## Slide 80
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 2 trays/ 1/3 hour = 6 trays/hour
Spatial Parallelism

## Slide 81
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour
Temporal Parallelism