## Slide 1: Sensors and Transducers
E80 Spring 2014
Erik Spjut

## Slide 2: Scientific & Engineering Measurements
Scientific Measurements
  What you measure with a rocket.
  What are examples?
Engineering Measurements
  What you measure about a rocket.
  What are examples?

## Slide 3: Experimental Measurements
Mass
Force
Acceleration
Velocity
Position
Displacement
Orientation
Vibration
EM Intensity
  Radio
  Microwave
  IR
  Visible
  UV
  X-ray
  Gamma

## Slide 4: Experimental Measurements II
Temperature
Pressure
Flow Rate
Composition
  Partial Pressure
  Humidity
  Mass fraction
  Mole fraction
  pH
Phases
  Aerosols
  Suspensions
  Microstructure
Sound
Images
Video

## Slide 5: Experimental Measurements III
Electrical
  Voltage
  Charge
  Current
  Resistance
  Inductance
  Capacitance
  Power
Time
Frequency
Phase
Angular
  Position
  Velocity
  Acceleration

## Slide 6: Digikey’s List of Sensors
Accelerometers (1022 items)
Accessories (3085 items)
Amplifiers (277 items)
Capacitive Touch Sensors, Proximity Sensor ICs (508 items)
Color Sensors (111 items)
Current Transducers (1440 items)
Dust Sensors (11 items)
Encoders (4042 items)
Flex Sensors (3 items)
Float, Level Sensors (313 items)
Flow Sensors (162 items)
Force Sensors (50 items)
Gas Sensors (66 items)
Gyroscopes (205 items)
Image Sensors, Camera (313 items)
Inclinometers (44 items)
IrDA Transceiver Modules (291 items)
LVDT Transducers (Linear Variable Differential Transformer) (47 items)
Magnetic Sensors - Compass, Magnetic Field (Modules) (26 items)
Magnetic Sensors - Hall Effect, Digital Switch, Linear, Compass (ICs) (2324 items)
Magnetic Sensors - Position, Proximity, Speed (Modules) (879 items)
Magnets (95 items)
Moisture Sensors, Humidity (257 items)
Motion Sensors, Detectors (PIR) (168 items)
Multifunction (101 items)
Obsolete/Discontinued Part Numbers (16 items)
Optical Sensors - Ambient Light, IR, UV Sensors (561 items)
Optical Sensors - Distance Measuring (36 items)
Optical Sensors - Mouse (117 items)
Optical Sensors - Photo Detectors - CdS Cells (38 items)
Optical Sensors - Photo Detectors - Logic Output (128 items)
Optical Sensors - Photo Detectors - Remote Receiver (1104 items)
Optical Sensors - Photodiodes (925 items)
Optical Sensors - Photoelectric, Industrial (2861 items)
Optical Sensors - Photointerrupters - Slot Type - Logic Output (1126 items)
Optical Sensors - Photointerrupters - Slot Type - Transistor Output (1115 items)
Optical Sensors - Phototransistors (738 items)
Optical Sensors - Reflective - Analog Output (323 items)
Optical Sensors - Reflective - Logic Output (123 items)
Position Sensors - Angle, Linear Position Measuring (937 items)
Pressure Sensors, Transducers (25455 items)
Proximity Sensors (3521 items)
RTD (Resistance Temperature Detector) (60 items)
Shock Sensors (11 items)
Solar Cells (82 items)
Specialized Sensors (311 items)
Strain Gages (24 items)
Temperature Regulators (3285 items)
Temperature Sensors, Transducers (1374 items)
Thermistors - NTC (4928 items)
Thermistors - PTC (1257 items)
Thermocouple, Temperature Probe (396 items)
Tilt Sensors (50 items)
Ultrasonic Receivers, Transmitters (78 items)
Vibration Sensors (30 items)

## Slide 7: What Spec’s Do We Care About?
Quantity Measured
Range or Span
Accuracy
Precision
Noise
Linearity
Speed of Response
Voltage Requirements
Current Requirements
Output Impedance
Mounting Requirements

## Slide 8: Example – Altimeter
Measure Absolute Pressure and Calculate Altitude
  What range of pressures do we need?
  What accuracy do we expect?

## Slide 9: Calculate Altitude from Pressure
http://en.wikipedia.org/wiki/File:Comparison_US_standard_atmosphere_1962.svg
US Standard Atmosphere

## Slide 10: For the Troposphere
where
  h = geopotential altitude (above sea level) (in meters)
  P0 = standard atmosphere pressure = 101325Pa
  T0 = 288.15K (+15°C)
  dT/dh = –0.0065 K/m: thermal gradient or standard temperature lapse rate
  R = 8.31432 Nm/mol K (Current NIST value 8.3144621)
  g = 9.80665 m/s²
  M = 0.0289644 kg/mol
From 1976 US Standard Atmosphere

## Slide 11: How Does Pressure Vary With Height?
Alt. (m) | Alt. (ft) | Alt. (mi) | P (Pa) | dP/dh (Pa/m)
0 | 0 | 0.000 | 101325 | -12.01
200 | 656 | 0.124 | 98945 | -11.78
400 | 1312 | 0.249 | 96610 | -11.56
600 | 1969 | 0.373 | 94321 | -11.34
800 | 2625 | 0.497 | 92076 | -11.12
1000 | 3281 | 0.621 | 89874 | -10.90
1200 | 3937 | 0.746 | 87715 | -10.69
1400 | 4593 | 0.870 | 85598 | -10.48
1600 | 5249 | 0.994 | 83522 | -10.27
1800 | 5906 | 1.118 | 81488 | -10.07
2000 | 6562 | 1.243 | 79494 | -9.87
2200 | 7218 | 1.367 | 77540 | -9.67
2400 | 7874 | 1.491 | 75624 | -9.48
2600 | 8530 | 1.616 | 73747 | -9.29

## Slide 12: Calculate Flight Height

## Slide 13: Assume 1 Mile AGL Max Alt
Lucerne Valley at 3000 ft MSL, Claremont 1200 ft
Pground = 90 kPa
Papogee = 74 kPa
Span = ∆P = 16 kPa
Need to allow for Barometric Pressure Changes +7% to –13%
Pmax = MAX(104 kPa, 97 kPa)
Pmin = 64 kPa

## Slide 14: MPXA6115AC7U
From Freescale Data Sheet

## Slide 15: Nominal Values
V @ Pmin= 0.200 V + (64 kPa – 15 kPa)0.045 V/kPa = 2.41 V
V @ Pmax = 0.200 + (104 kPa – 15 kPa)0.045 V/kPa = 4.21 V
Accuracy (Uncalibrated) ±1.5% VFS = ±1.5%4.7 V = ±0.071 V = ±1.57 kPa = ±157 m
tR10%-90% = 1.0 ms, τ = tR10%-90%/ln(9) = 0.46 ms

## Slide 16: Output Impedance
Can drive circuit with 0.5 mA at 4.7 V
Impedance of driven circuit = V/I = 4.7 V/0.0005 A = 9400 Ω.
Actual output impedance determined empirically. How?

## Slide 17: Choices on Conditioning
Data Logger
  0 V to 3.3 V
  Input Impedance ~2200 Ω
  16 bit, 1 LSB = 3.3 V/216 = 50 µV
Change gain so Vmax = 3.3 V
  1 LSB = 50 µV = 0.16 m = 6 in
Change gain and offset so Vmin = 0 V & Vmax = 3.3 V
  1 LSB = 50 µV = 0.06 m = 2.4 in

## Slide 18: Signal Conditioning
Does it need a buffer amp? How would you know?
How do you change the gain?
How do you change the gain and offset?
What about aliasing?

## Slide 19: Single-Sided Circuits
Data logger expects 0 V to 3.3 V signals
Classical op-amp circuit power ±15 V
Low-voltage op-amp circuit power
  ±1.4 V to ±3 V
  0-to-2.8 V to 0-to-6 V
Signal offset
Reference offset
Virtual ground
(Will visit again under Flight Hardware)

## Slide 20: Inverting Amps

## Slide 21: Non-Inverting Amps

## Slide 22: Can You do Single Sided for:
Differential Amplifier?
Integrator?
Transimpedance Amplifier?
Sallen-Key Filter?
Bipolar sensor like piezoelectric vibration?

## Slide 23: Example – Gas Sensor
MQ-2 CH4 Gas Sensor (Digikey, Parallax, or Pololu)

## Slide 24: Other Specs

## Slide 25: Sensitivity

## Slide 26: Power Calculations
5 V @ 800 mW = 160 mA.
5 V @ 33 Ω = 150 mA.
Standard 9 V battery is ~250 mAh
  Would last about 1 ½ hours
  Separate battery for sensor and system.

## Slide 27: Signal Conditioning
Must get air to sensor.
Resistance changes with gas concentration.
Designed to work in voltage divider.
Need R in range of approx. 3 kΩ to 30 kΩ.
Need buffer amp.
What is time constant?
http://www.parallax.com/catalog/sensors/gas for more info

## Slide 28: Example – Particle Sensor

## Slide 29: Driving & Reading Circuits

## Slide 30: Output & Caution

## Slide 31: Driving Circuit

## Slide 32: Reading Circuit
Pulse Width 0.32 ms
Minimum 1 point
Best 10 points
Sample rate = 10/0.32 ms = 31.25 kSPS

## Slide 33: Could You Do Better?
IRED and Driver
Photodiode & Reading Circuit
Mechanical & Optical Chamber
Start at http://en.wikipedia.org/wiki/Particle_counter for more information

## Slide 34: Example – Humidity Sensor
Check out Digikey
  http://www.digikey.com/product-search/en?FV=fff4001e%2Cfff80274&mnonly=0&newproducts=0&ColumnSort=1000011&page=1&stock=0&pbfree=0&rohs=0&quantity=1&ptm=0&fid=0&pageSize=25
Digital, I2C – 18 s response time
Capacitive – 15 s, 5 s response time
Linear Voltage – 5 s response time

## Slide 35: Digital, I2C
Need microcontroller, e.g., Arduino Pro Mini 328 - 3.3V/8MHz <Sparkfun>
Power separately from data logger
Must synchronize
Must program

## Slide 36: Capacitive
How do you measure capacitance?
  Put in a timer circuit
  Put in an integrator
  Put in a voltage divider

## Slide 37: In a Timer Circuit

## Slide 38: Honeywell HIH-1000-002

## Slide 39: Measurement Calc’s
R | 200,000 | Ω
C | 330 | pF
 | 3.3E-10 | F
RC | 0.000066 | s
 | 66 | µs
Angular Freq | 15152 | s–1
Freq | 2411 | Hz
Sensitivity | 0.6 | pF/%RH
0% RH | 297 | pF
 | 2679 | Hz
100% RH | 357 | pF
 | 2229 | Hz
∆F | 450 | Hz
∆F/F | 18.67% | Hz/Hz
The sample rate will need to be high enough to discriminate the frequency changes.

## Slide 40: Integrator
From: http://www.radio-electronics.com/info/circuits/opamp-circuits/operational-amplifier-integrator.php

## Slide 41: Issues
Easiest input is constant voltage
  Output is then a ramp
  Calculate C from ramp slope or time to Vset.
How control reset switch?
  Solid State Relay
  Signal Generator
  Comparator

## Slide 42: Voltage Divider
Need sinusoidal input

## Slide 43: Voltage Divider Performance

## Slide 44: How Do You Generate a Sine Wave?

## Slide 45: How Do You Generate a Sine Wave?

## Slide 46: Linear Voltage

## Slide 49
The challenges are how and where to connect it, how and where to mount it, and how to get airflow over it.

## Slide 50: Where to look for sensors
Digikey: http://www.digikey.com
Mouser: http://www.mouser.com
Arrow: http://www.arrow.com
Sparkfun: https://www.sparkfun.com
Pololu: https://www.pololu.com
Parallax: http://www.parallax.com