## Slide 1: Flight Hardware
E80 Spring 2013
Erik Spjut

## Slide 2: NASA Standards
Mechanical tests
  Strength
  Sinusoidal sweep vibration (5 to 50 hertz [Hz]) ELV and STS payloads
  Random vibration and acoustics
  Shock (mechanical and pyro)
  Modal survey
  Pressure profile
  Appendage deployment
Thermal tests
  Thermal/vacuum and ambient pressure thermal cycling
  Thermal balance
  Bakeout
  Leak test for sealed components
EMI tests
Functional tests
  Electrical interface
  Comprehensive performance
  Failure-free performance
  End-to-end compatibility tests and mission simulations
  Life test program
  Mass properties verification

## Slide 3: E80 Engineering Requirements
Payload Dimensions
Power Requirements
Acceleration, Shock, & Vibration
Temperature Profile
Speed of Response
Sensor Requirements
Construction Standards

## Slide 4: Payload Dimensions
PC Board & Envelope
  1.80” by 10.10” (height depends on components)
Aerotech
  ID 1.800”
  Length Arreaux 12”, Barracuda 22.75”

## Slide 5: Payload Dimensions
PC Board & Envelope
  1.80” by 10.10” (height depends on components)
PML – 12´´Payload Bay
  Length 11.75” to 11.88”
  ID Tube 2.152”
  ID Coupler 2.02”

## Slide 6: Power Requirements
Power Inputs
  Data Logger: 6 V to 20 V
  IMU: 5 V (regulated) & 3 V to 3.3 V (regulated)
  AD623AN: 3 V to 12 V or ±1.5 V to ±6 V
  MPC 60XX: 2.7 V to 6 V
  Other sensors – TBD
Must measure current draw of final circuit.
Batteries must power for 1 hour minimum.
Turn on before launch, stay on during flight, turn off after recovery.

## Slide 7: Power (cont)
Power sources
  9 V lithium, 750 mAh
  1.5 V
    AAA Alkaline, 1000 mAh; Lithium, 1200 mAh
    AA Alkaline, 2700 mAh; Lithium, 3000 mAh
  12 V (NEDEA- 1811A), 55 mAh
References
  Duracell Tech Specs
  Energizer Tech Specs

## Slide 8: Power (cont)
Rechargable Batteries
  LiPo (High Power Density, Special Charger, HazMat)
    3.7 V, up to 5000 mAh
    7.4 V, up to 5000 mAh
    11.1 V, up to 5000 mAh
  NiMH
  NiCd

## Slide 9: Acceleration, Vibration, & Shock
Acceleration
  From motor, 6 G to 50 G
    Use RockSim or OpenRocket to estimate
Shock
  From deployment charge, 2 G to 20 G
  From parachute, 1 G to 50 G
  From ballistic landing, 200 G +

## Slide 10: Vibration
From motor
From aerodynamics
From shock impulse
Amplified at resonant frequencies
Viscoelastic damping materials

## Slide 11: Temperature Profile
Standards
  Commercial Grade: 0°C to 70°C
  Industrial Grade: –40°C to 85°C
  Military Grade: –55°C to 125°C
Launch
  Often –2°C at 6 AM
  Solar heating of payload section to 50°C+
  At standard lapse rate ∆T = –7.8°C @ 1200 m AGL

## Slide 12: Sensor Requirement
Minimum 2 types of sensors
  2 Thermocouples wouldn’t count
  1 Thermocouple, 1 thermistor would (but see next)
Minimum 1 sensor with BW ≥ 1 kHz
Necessary speed of response
Mechanical Integrity (launch, flight, recovery)
Functional Placement

## Slide 13: Speed of Response
Sensor adequate:
Needs deconvolution:
Hopeless:

## Slide 14
PML Phobos on H123W-M, Effect of T-sensor Time Constant
Chart: Time (seconds)

## Slide 15
PML Phobos on H123W-M, Hysteresis of T-sensor
Chart: Altitude (feet)

## Slide 16: Sensor Requirement (cont.)
Air Temperature
  Sensor in free stream
Pressure Altimeter
  No Flow
  Pressure taps, 3 or 4 symmetric
Gas/Humidity Sensor
  Gas flow to sensor

## Slide 17: Pitot- Static Tube
Pitot Tube
  In free stream
  In direction of motion
Static Tap
  Normal to flow
  Preferable 4+ calibers from nose cone
  Multiple in symmetric pattern best

## Slide 18: Pitot Tube Designs
http://naca.central.cranfield.ac.uk/reports/arc/rm/3365.pdf

## Slide 19: Sensor Requirements (cont)
Light Sensor
  Proper orientation
  Proper view field
Vibration Sensor
  Best on anti-node
  Avoid node
  Not for DC strain

## Slide 20: Sensor Requirements (cont)
Particle/Dust Sensor
  Gas flow through sensor
  If optical, reduce or eliminate background reflections/light.
  Often needs pulse train
Accelerometer/ Rate Gyroscope
  Known fixed orientation
  Means to deal with baseline and drift

## Slide 21: Sensor Placement
Easiest in Payload Section
Next easiest in Nosecone
Ports/Channels to rout to exterior
Don’t forget separation for recovery
  Can run (very long) wires through shock cord
  Can make connector that separates at recovery
  Can have separate sections

## Slide 22: Video Camera
Battery charged by USB
40 minute battery time on full charge
Creates 720P .mov file on microSD
10 minutes per 1 GB. On 16 GB card will run out of battery before storage
Physical Mounting
  Method
  Location
  Field of View

## Slide 23: Data Logger
Created and programmed by Tyler Smelt
16 channels
16-bit resolution
Max 400 kSPS composite rate (25 kSPS/chan)
Max 200 kSPS on single channel

## Slide 24: Data Logger
Power with 6 V to 20 V (9 V recommended)
Uses microSD for storage (have 16 GB cards)
Input range 0 to 3.3 V
Input Impedance ≈2.2kΩ
Set parameters with Config File
Have VI and .m file to read binary data files
PIC-32 microcontroller
2 – AD7689 A/D

## Slide 25: Single-Sided Circuits
Data logger expects 0 V to 3.3 V signals
Classical op-amp circuit power ±15 V
Low-voltage op-amp circuit power
  ±1.4 V to ±3 V
  0-to-2.8 V to 0-to-6 V
Signal offset
Reference offset
Virtual ground

## Slide 26: Inverting Amps

## Slide 27: Non-Inverting Amps

## Slide 28: PC Board
Top laid out like your protoboard
  4 exterior buses slightly closer
  1 extra power bus
Bottom has connectors for data logger
4 Holes for mounting
2 holes for mounting battery holder

## Slide 29: PC Board
Center has place for 5 V regulator + three more
Regulators can tie common to ground or not.
Bottom has connectors for data logger

## Slide 30: Rocket Assignments
Team 1 – PML Phobos <.rkt> <.ork>
Team 2 – Aerotech Arreaux <.rkt> <.ork>
Team 3 – PML X-Calibur <.rkt> <.ork>
Team 4 – Aerotech Barracuda <.rkt> <.ork>
Team 5 – PML Phobos <.rkt> <.ork>
If you feel you need a rocket different from the assigned, write a proposal explaining the technical reasons and give it to your section prof.

## Slide 31: Rocket Construction
NAR or TRA safety Code is mandatory.
Materials: I will use only lightweight materials such as paper, wood, rubber, plastic, fiberglass, or when necessary ductile metal, for the construction of my rocket.
Motors: I will use only certified, commercially made rocket motors, and will not tamper with these motors or use them for any purposes except those recommended by the manufacturer. I will not allow smoking, open flames, nor heat sources within 25 feet of these motors.

## Slide 32: Rocket Construction (cont.)
Adhesives must be used under fume hood, in spray-paint booth, or outdoors.
Neoprene gloves required. Eye protection recommended
G10 Fiberglass (PML fins) must be wet sanded or with full respiratory protection. Neoprene gloves strongly recommended.
No sharp implements permitted when removing plastic rivets.

## Slide 33: Rocket Construction (cont.)
Spray painting only permitted in paint booth or outdoors. Skin & eye protection recommended.
If you follow the unmodified instructions for the rockets, you will not be able to fly them.
  PML requires motor retainer, modified motor mount placement, and launch rail guides.
  Aerotech requires motor retainer, longer motor mount, modified placement, and removal of motor hook, thrust ring, and thrust ring flange

## Slide 34: Rocket Construction (cont.)
Motor retainers attached with JB Weld ONLY!
Epoxy (PML kits)
  Surfaces to be joined must be pre-sanded with 80-to-120 grit sandpaper (and then de-dusted).
  Mix small quantities at a time (exothermic reaction)
  Epoxy flows until fully set
Epoxy clay
  Not quite as strong as epoxy
  Very useful for fillets and custom mounts
  You always need less than you think

## Slide 35: Rocket Construction (cont.)
Cyanoacrylic/Super-Glue (Aerotech)
  Make SURE you have adequate ventilation
  ALWAYS use skin protection (neoprene gloves)
  Usually sets in 30 s to 20 min
  Can use accelerator (we have limited supplies)
  Accelerator on one surface + Super-Glue on other surface = instant bond when joined.
  Will have to dribble on some internal joints

## Slide 36: Rocket Hints
The PML Piston Strap is in the Piston parts..
For PML kits, make sure fins are straight.
  Use masking tape.
  Use patience.

## Slide 37: Rocket Hints (cont.)
For Aerotech kits, there is no need for the 24 mm motor adaptor.
For Aerotech kits, make sure the fins snap easily into the Fink Locks BEFORE putting the Motor Tube Assembly into the Body Tube.
For Aerotech kits, it’s very difficult to reconnect the shock cord to the nose cone. An extension from the screw eye to the end of the coupler makes the process much easier.

## Slide 38: Payload Sections
PC board designed to fit in PML payload bay.
PC board matches Aerotech body tubing diameter.
A 14.75´´ long Aerotech body tube fits the PC board.
Arreaux payload section too short.
Barracuda payload section too long.
We have extras of both PML and Aerotech to allow for mistakes.

## Slide 39: Deliverables
Week 1
  Scientific and/or Engineering objectives
  Complete schematic
  Parts list (especially to order)
  Check off by Section Prof & Prof Spjut
Week 2
  Complete protoboard
  Measured current draw
  Demonstrate functionality
  Check off by Section Prof & Prof Spjut

## Slide 40: Deliverables (cont.)
Week 3
  Fully populated PC board
  Demonstrate functionality
  Check off by Section Prof & Prof Spjut
Week 4
  Completed Rocket
  Complete ground and analysis procedures
  Completed launch checklist (you have to DO steps)
  Loaded launch motors

## Slide 41: Deliverables (cont.)
Week 5
  List lessons learned
  Fix & correct things
  Load launch motors
Week 6
  Analyze data
  Write Final Report
  Prepare Final Presentation