## Slide 1: Engineering 80 – Spring 2015 Flight Hardware

## Slide 2: Three Words You Should Know!
MAKE IT HAPPEN

## Slide 3: MAKING IT HAPPEN

## Slide 4: Three Words You Should Know!
“MAKE IT HAPPEN”?
How does one

## Slide 5: What’s Your Problem Statement?
SOURCE: http://www.clker.com/cliparts/6/5/b/f/11949864691020941855smiley114.svg.med.png

## Slide 6: A “ONE-PAGER”…
  Problem Statement (or Purpose, or Goal)
    The final E80 project needs to be completed to pass the course
  Success Criteria (envision successfully crossing the finish line)
    Design, build, and test a rocket that meets E80 requirements, and submit a final report and give a final presentation
  Strategies (how are you going to get to that finish line?)
    Work as a team to meet all weekly project deliverables
  Timeline (detailed plan for implementing the strategies)
TASK | Start | End | Status
Meet Week 1 Deliverables | 3/12/2015 | 3/25/2015 | In Progress
Meet Week 2 Deliverables | 3/25/2015 | 4/1/2015 | Not Started
Meet Week 3 Deliverables | 4/1/2015 | 4/8/2015 | Not Started
Meet Week 4 Deliverables | 4/8/2015 | 4/15/2015 | Not Started
Meet Week 5 Deliverables | 4/15/2015 | 4/22/2015 | Not Started
Meet Week 6 Deliverables | 4/22/2015 | 5/4/2015 | Not Started
Give Final Presentation | 5/4/2015 | 5/4/2015 | Not Started
Sample Timeline for Section 2

## Slide 7: Today We Will Discuss…
E80 Rocket Requirements
Surviving Launch and Recovery
Rocket Construction
Deliverables

## Slide 8: E80 Engineering Rocket Requirements
Payload Dimensions
Sensor Requirements
Speed of Response
Power Requirements
Acceleration, Shock, and Vibration
Temperature Profile
Construction Standards

## Slide 9: Payload Dimensions
You will be assigned either an…
  Aerotech Arreaux <.rkt> <.ork> <.zip>
    Payload Section ID: 1.80 inches
    Payload Section Length: 12.00 inches
  Aerotech Barracuda <.rkt> <.ork> <.zip>
    Payload Section ID: 1.80 inches
    Payload Section Length: 22.75 inches
ID = 1.80”
Length = 12” -or- 22.75”
If you feel you need a rocket different from the assigned, write a proposal explaining the technical reasons and give it to your section Prof.
Teams
1, 3, & 5
Teams
2 & 4

## Slide 10: Your Precious Payload – The PC Board
Top laid out like your protoboard
  4 exterior buses slightly closer
  1 extra power bus
Bottom has connectors for a data logger
4 Holes for mounting
2 holes for mounting battery holder
If it works on your protoboard, then it will work on the PC Board Chip for Chip
Wire for Wire

## Slide 11: Payload Sections
PC board matches Aerotech body tubing diameter
Arreaux payload section too short
Barracuda payload section too long
An Aerotech body tube that fits the PC board will be provided
ID = 1.80”
Length = 10.10”

## Slide 12: Data Logging
How do you acquire and log data in the rocket?
ID = 1.80”
Length = 10.10”

## Slide 13: Your Precious Payload – The PC Board
Center has place for 5 V regulator + three more
Regulators can tie common to ground or not
Bottom has connectors for data logger

## Slide 14: Your Precious Payload – The Data Logger
Created and programmed by Tyler Smelt
16 channels (Can measure up to 16 sensors)
16-bit resolution
Max 400 kSPS composite rate (25 kSPS/chan)
Max 200 kSPS on single channel (read in pairs)
Power with 6 V to 20 V (9 V recommended)
Uses microSD for storage (have 16 GB cards)
  Need to tape/secure the SD card in the reader!
Input range 0 to 3.3 V
Input Impedance ≈2.2kΩ (MyDAQ is 10 GΩ)
  Low impedance, may need to buffer your input signals
Set parameters with Config File (Initialize on PC)
Have VI and .m file to read binary data files
PIC-32 microcontroller; Two AD7689 A/D Chips
MORE INFO ON THE E80 WEBSITE!

## Slide 15: Single–Sided Circuits
Data logger expects 0 V to 3.3 V signals
Classical op-amp circuit power ±15 V
Low-voltage op-amp circuit power
  ±1.4 V to ±3 V
  0-to-2.8 V to 0-to-6 V
Signal offset
  Normal signal that goes above and below zero will need DC offset
Reference offset
Virtual ground
  This is where we want all signals referenced
  WHAT IS A VIRTUAL GROUND?

## Slide 16: Inverting Amps
LOW POWER OP-AMP

## Slide 17: Inverting Amps
What are these for?
LOW POWER OP-AMP

## Slide 18: Inverting Amps
These filter out noise in the power lines; Use them!
LOW POWER OP-AMP

## Slide 19: Inverting Amps
LOW POWER OP-AMP

## Slide 20: Inverting Amps
Virtual Ground
This offsets the op-amp so that the signal is centered between 0 and 5 V
Low side of battery
High side of battery
LOW POWER OP-AMP

## Slide 21: Inverting Amps
Virtual Ground
This offsets the op-amp so that the signal is centered between 0 and 5 V
Low side of battery
High side of battery
If you are powering your circuit by battery and you have a single sided supply, you need to think of creating a virtual ground halfway between your low and high on your op amp; then offset your signal so that you have your average value in the middle instead of zero
Data logger needs 0 to 3.3 V;
You could go from 0 to 3.3 V with 1.8 V as center
LOW POWER OP-AMP

## Slide 22: Non-Inverting Amps

## Slide 23: Scientific vs. Engineering Measurements
WHAT’S THE DIFFERENCE?

## Slide 24: Scientific vs. Engineering Measurements
Engineering Measurements
“What you measure about a rocket.”
Scientific Measurements
“What you measure with a rocket.”

## Slide 25: Sensor Requirement
You are required to have a MINIMUM of 2 types of sensors
  One thermocouple and one thermistor would count
  Two thermocouples would NOT count

## Slide 26: What Does a PC Board with Sensors Look Like?
WHERE WOULD I FIND THIS?

## Slide 27: What Does a PC Board with Sensors Look Like?
SOURCE: http://www.eng.hmc.edu/NewE80/LargePhotos/KC20120421_IMG_1658.jpg

## Slide 28: Sensor Requirement
You are required to have a MINIMUM of 2 types of sensors
  One thermocouple and one thermistor would count
  Two thermocouples would NOT count
SOURCE: http://www.eng.hmc.edu/NewE80/LargePhotos/KC20120421_IMG_1658.jpg

## Slide 29: Speed of Sensor Response
We recommend using…
  At least one sensor with a time constant faster than 1 ms
    Bandwidth ≥ 1 kHz
  Sensor adequate:
    The bandwidth of the sensor is 10 times higher than the phenomenon that you want to measure
  Sensor Needs deconvolution:
  Sensor is “Hopeless”:

## Slide 30: Effect of Temperature Sensor Time Constant

## Slide 31: Temperature Measurement Devices in Lab
>

## Slide 32: Effect of Temperature Sensor Time Constant
PML Phobos on H123W-M
Effect of Temp. Sensor Time Constant
  At standard lapse rate
  ∆T = –7.8°C @ 1200 m AGL
  Temperature drops by 0.0065oC for every meter going up

## Slide 33: Effect of Temperature Sensor Time Constant
PML Phobos on H123W-M
Effect of Temp. Sensor Time Constant
PML Phobos on H123W-M
Hysteresis of Temp. sensor

## Slide 34: Actual Data from Sensors

## Slide 35: Actual Data from Sensors
Speed of Sound = 343 m/s

## Slide 36: Actual Data from Sensors

## Slide 37: Actual Data from Sensors
WHY THE DISCREPANCY?

## Slide 38: Actual Data from Sensors
Pnut assumes Standard Atmospheric Model
Dry Air
Temperature Varies Linearly

## Slide 39: Sensor Requirement
You are required to have a MINIMUM of 2 types of sensors
  One thermocouple and one thermistor would count
  Two thermocouples would NOT count
WHAT OTHER TYPES OF SENSORS COULD WE USE?
  Pressure Altimeter
  Pitot-Static Tube
  Gas/Humidity Sensor
  Vibration Sensor; Light Sensor

## Slide 40: Sensor Requirement
You are required to have a MINIMUM of 2 types of sensors
  One thermocouple and one thermistor would count
  Two thermocouples would NOT count
WHAT OTHER TYPES OF SENSORS COULD WE USE?
  Pressure Altimeter
  Pitot-Static Tube
  Accelerometer/Rate Gyroscope
  Gas/Humidity Sensor; Vibration Sensor; Light Sensor

## Slide 41: Sensor Requirements
Air Temperature Sensor
  Sensor in the free stream
Pressure Altimeter
  No flow; 3 or 4 symmetric pressure taps
Accelerometer/Rate Gyroscope
  Known fixed orientation
  Means to deal with baseline and drift
Pitot-Static Tube
  Pitot tube in free stream and direction of motion
  Static Tap should be normal to the flow
    Preferable 4+ “calibers” (rocket tube diameters) from the nose cone
    Multiple in symmetric pattern is best
SOURCE: http://www.ipscustom.com/ProdImages/Wire_E_tt_pp_m.gif
SOURCE: http://web.stanford.edu/class/me220/data/lectures/lect05/static_probe.gif
SOURCE: http://cdn2.bigcommerce.com/server2900/730e2/products/56/images/248/PnutTop__64333.1405342120.1280.640.png?c=2
Your Team has a Budget of $50

## Slide 42: Sensor Requirements
Light Sensor
  Proper orientation and view field
Vibration Sensor
  Best on anti-node; avoid node
  Nor for DC strain
Gas Humidity Sensor
  Gas flow to sensor is desired
Particle/Dust Sensor
  Gas flow through sensor
  If optical, reduce or eliminate background light
  Often needs pulse train
SOURCE: http://www.digikey.com/product-detail/en/HIH-5030-001/480-3294-1-ND/2061078
SOURCE: http://www.digikey.com/product-search/en?vendor=0&keywords=605-00004-ND
SOURCE: http://www.digikey.com/product-detail/en/GP2Y1010AU0F/425-2068-ND/720164

## Slide 43: Sensor Placement
Sensors need to be placed in locations where a measurement is desired
Easiest in Payload Section
Next easiest in Nosecone
Ports/Channels to rout to exterior
Don’t forget separation for recovery
  Can run (very long) wires through shock cord
  Can make connector that separates at recovery
  Can have separate sections

## Slide 44: What Does a Rocket with Sensors Look Like?
WHERE WOULD I FIND THIS?

## Slide 45: What Does a Rocket with Sensors Look Like?
SOURCE: http://www.eng.hmc.edu/NewE80/LargePhotos/20140419_E80-FirstLaunch_SMM_341.jpg

## Slide 46: Video Camera
Battery charged by USB
40 minute battery time on full charge
Creates 720P .mov file on microSD
10 minutes per 1 GB
  On 16 GB card will run out of battery before storage
Physical Mounting
  Method
    Duct tape? Electrical tape?
  Location
    Center of pressure?
  Field of View

## Slide 47: Power Requirements
Power Inputs
  Data Logger: 6 V to 20 V
  IMU: 5 V (regulated) & 3 V to 3.3 V (regulated)
  AD623AN: 3 V to 12 V or ±1.5 V to ±6 V
  MPC 60XX: 2.7 V to 6 V
  Other sensors – TBD
Must measure current draw of final circuit
Batteries must power for 1 hour minimum
  Battery capacity (in mAh) / Average current consumption (in mA) = Hours of expected runtime
Turn on before launch, stay on during flight, turn off after recovery.

## Slide 48: Power Sources
Power sources
  9 V lithium, 750 mAh
  1.5 V
    AAA Alkaline, 1000 mAh; Lithium, 1200 mAh
    AA Alkaline, 2700 mAh; Lithium, 3000 mAh
  12 V (NEDEA- 1811A), 55 mAh
  LiPo (Rechargable, High Power Density, Special Charger, HazMat)
    3.7 V, up to 5000 mAh
    7.4 V, up to 5000 mAh
    11.1 V, up to 5000 mAh
  NiMH (Rechargable)
  NiCd (Rechargable)
Your team will decide on which power source to use
Your Team has a Budget of $50

## Slide 49: Surviving
What does your rocket have to survive during launch?
BE THE ROCKET

## Slide 50: Temperature
1) Temperature at Launch
  Often –2°C at 6 AM
  Solar heating of payload section to 50°C+
  At standard lapse rate ∆T = –7.8°C @ 1200 m AGL
    Temperature drops by 0.0065oC for every meter going up
Standards for Parts
Commercial Grade: 0°C to 70°C
Industrial Grade: –40°C to 85°C
Military Grade: –55°C to 125°C

## Slide 51: Acceleration
2) Acceleration
  From motor, 6g to (50+)g
  Use RockSim or OpenRocket to estimate

## Slide 52: Vibration
3) Vibration (What causes vibration?)
BE THE ROCKET

## Slide 53: Vibration
3) Vibration (What causes vibration?)
  From motor
  From aerodynamics
  From shock impulse
  Amplified at resonant frequencies
  Use viscoelastic damping materials
SOURCE: http://www.sorbothane.com/blog/wp-content/uploads/2010/07/engine-vibrations.jpg

## Slide 54: Shock
4) Shock (What causes shock?)
BE THE ROCKET

## Slide 55: Shock
4) Shock (What causes shock?)
  Deployment charge, 2 g to 20+ g
  From parachute, 1 g to 50+ g
  From ballistic landing, 200+ g

## Slide 56: Surviving
What does your rocket have to survive during launch?
  Temperature
  Acceleration
  Vibration
  Shock

## Slide 57: Constructing Your Rocket
NAR or TRA safety Code is mandatory.
Materials: I will use only lightweight materials such as paper, wood, rubber, plastic, fiberglass, or when necessary ductile metal, for the construction of my rocket.
Motors: I will use only certified, commercially made rocket motors, and will not tamper with these motors or use them for any purposes except those recommended by the manufacturer. I will not allow smoking, open flames, nor heat sources within 25 feet of these motors.

## Slide 58: Constructing Your Rocket
Adhesives must be used under fume hood, in spray-paint booth, or outdoors.
Neoprene gloves required. Eye protection required
G10 Fiberglass (PML fins) must be wet sanded or with full respiratory protection. Neoprene gloves strongly recommended.
No sharp implements permitted when removing plastic rivets.
Spray painting only permitted in paint booth or outdoors (not by Libra Complex). Skin & eye protection required.
If you follow the unmodified instructions for the rockets, you will NOT be able to fly them.
  Aerotech requires motor retainer, longer motor mount, modified placement, and removal of motor hook, thrust ring, and thrust ring flange

## Slide 59: Rocket Construction
Motor retainers attached with JB Weld ONLY!
Cyanoacrylic/Super-Glue (Aerotech)
  Make SURE you have adequate ventilation
  ALWAYS use skin protection (neoprene gloves)
  Usually sets in 30 s to 20 min
  Can use accelerator (we have limited supplies)
  Accelerator on one surface + Super-Glue on other surface = instant bond when joined.
  Will have to dribble on some internal joints
Epoxy clay
  Not quite as strong as epoxy
  Very useful for fillets and custom mounts
  You always need less than you think

## Slide 60: Rocket Hints
For Aerotech kits…
  There is no need for the 24 mm motor adaptor.
  Make sure the fins snap easily into the Fink Locks BEFORE putting the Motor Tube Assembly into the Body Tube.
  It’s very difficult to reconnect the shock cord to the nose cone. An extension from the screw eye to the end of the coupler makes the process much easier.

## Slide 61: Deliverables
Week 1
  Scientific and/or Engineering objectives
  Select sensors (min: 2, MAX: 16)
  Parts list (especially to order)
  Complete schematic
    Show all calculations; bypass capacitors; power
  Check off by Section Prof & Prof Spjut
Week 2
  Complete protoboard
  Measured current draw
  Demonstrate functionality
  Check off by Section Prof & Prof Spjut
NO RESTRICTIONS ON WHEN YOU DO YOUR WORK.
However, priority for resources goes to groups that were assigned to that lab section.
Need to show up to your lab section for the check-off.

## Slide 62: Deliverables
Week 3
  Fully populated PC board
  Demonstrate functionality
    Data acquisition works and is demonstrated
  Check off by Section Prof & Prof Spjut
Week 4
  Completed Rocket
  Complete ground and analysis procedures
  Completed launch checklist (you have to DO steps)
  Loaded launch motors
NO RESTRICTIONS ON WHEN YOU DO YOUR WORK.
However, priority for resources goes to groups that were assigned to that lab section.
Need to show up to your lab section for the check-off.

## Slide 63: Deliverables
Week 5
  List lessons learned
  Fix & correct things
  Load launch motors
Week 6
  Analyze data
  Write Final Report
  Prepare Final Presentation
NO RESTRICTIONS ON WHEN YOU DO YOUR WORK.
However, priority for resources goes to groups that were assigned to that lab section.
Need to show up to your lab section for the check-off.

## Slide 64: A “ONE-PAGER”…
  Problem Statement (or Purpose, or Goal)
    The final E80 project needs to be completed to pass the course
  Success Criteria (envision successfully crossing the finish line)
    Design, build, and test a rocket that meets E80 requirements, and submit a final report and give a final presentation
  Strategies (how are you going to get to that finish line?)
    Work as a team to meet all weekly project deliverables
  Timeline (detailed plan for implementing the strategies)
TASK | Start | End | Status
Meet Week 1 Deliverables | 3/12/2015 | 3/25/2015 | In Progress
Meet Week 2 Deliverables | 3/25/2015 | 4/1/2015 | Not Started
Meet Week 3 Deliverables | 4/1/2015 | 4/8/2015 | Not Started
Meet Week 4 Deliverables | 4/8/2015 | 4/15/2015 | Not Started
Meet Week 5 Deliverables | 4/15/2015 | 4/22/2015 | Not Started
Meet Week 6 Deliverables | 4/22/2015 | 5/4/2015 | Not Started
Give Final Presentation | 5/4/2015 | 5/4/2015 | Not Started
Sample Timeline for Section 2

## Slide 65: Good Luck Over the Next 7 Weeks!
MAKE IT HAPPEN!